## Slide 1
CAN Bus
Marcel Breitenfellner, Jürgen Punz | 14. Juni 2017

## Slide 2: General
  Automotive Bus System
  Connecting ECUs
  Producer/Consumer System (like Publisher/Subscriber)
  Standardized since 1994 (ISO11898)
  Two transmission rates
    125kbit/s (convenience)
    1MBit/s (powertrain, chassis area, time critical)
  Reliable protocol in harsh conditions
  1.5V – 3.5V level
CAN (Controller Area Network)

## Slide 3: General
OSI Model

## Slide 4: General
Maximum Length

## Slide 5: General
  Transmission hardware for bus access
  Software for CAN Protocol
  Differential transmission
    More robust to interference
Transmission

## Slide 6: General
  CRC for data protection
    Transmission errors can be detected
  Receiver ACKs the message (+CRC)
  Synchronized through edge transitions
  Maximum 130bits in length (fast reaction with 1MBit/s)
Frame

## Slide 7: General
  Real-time transmission is important
    In low milliseconds range
    Depends on occurence of special events
    130µS per frame
  With high bus load the risk of collisions rises
  Carrier Sense Multiple Access/Collision Avoidance (CSMA/CA) is used
    If collision higher priority wins
    Low priority frames could be delayed
Communication

## Slide 8: General
  CRC over each frame + ACK/NACK
  Form check, stuff check
  Transmission error on HW level
    Error flag
    Immediate stop
    All transmissions are aborted
    As soon as available try again
Data Protection

## Slide 9: General
  Arduino Shield available
    Starting at 10$ in China
  ESP8266 Dev Board
    IoT your card
    Starting at 10$ in China
  OBD2 Bluetooth
  ~10€ on Amazon
Bridge

## Slide 10: Q&A
  http://vector.com/portal/medien/cmc/press/PTR/ SerielleBussysteme Teil2 ElektronikAutomotive 200612 PressArticle DE.pdf
  http://vector.com/portal/medien/cmc/press/PressReport-SerielleBussysteme-DE.pdf
  https://elearning.vector.com/portal/medien/cmc/press/PTR/ SerialBusSystems Part4 ElektronikAutomotive 200703 PressArticle EN.pdf
  https://elearning.vector.com/vl sbs introduction en.html
  http://www.digikey.com/en/articles/techzone/2014/jul/
  what- engineers- need- to- know- when- selecting- an- automotive- qualified- mcu- for- vehicle- applications